## Slide 1: Layer 2 technologies advanced
Lecture 1
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Spanning tree protocol advanced: MSTP and PVST+
Link aggregation
Device stacking: IRF

## Slide 3
Spanning tree protocol advanced

## Slide 4: What is the Spanning Tree Protocol?
It addresses a problem which switches can not handle alone: the broadcast storms
Without STP, a L2 loop will:
    Overload the links
    Affect the end devices
    Cause MAC table instability
    …never stop

## Slide 5: The STP algorithm
Elect the Root switch (Root bridge)
    This is the switch with the lowest BID (Bridge ID)
    BID = Switch Priority and MAC
Select the root ports
    They have the best cost (lowest) to the Root
    Selected per switch
Select the designated ports
    They have the best cost (lowest) to the Root
    Selected per segment (connection)
All other ports go to blocking state

## Slide 6: STP tie-breakers
If there is a tie situation - the same path cost via different paths, use the following tie-breakers:
    When selecting Root port or Designated port, chose the neighboring switch which has the lowest Bridge ID
    If the Bridge ID is the same, select the lowest Port ID (PID)
    Port ID = Port priority and port number

## Slide 7: Spanning Tree Protocol – Main Flavors
STP - Spanning Tree Protocol, IEEE 802.1D
RSTP - Rapid STP, IEEE 802.1W
MSTP - Multiple STP, IEEE 802.1S (802.1Q-2005)
PVST+ - Per-VLAN STP, Cisco proprietary

## Slide 8: MSTP
Multiple Spanning Tree Protocol
Creates multiple instances of the physical STP topology
Can have different Root switches - one for each instance
Provides load-sharing because of the multiple Roots
It is also “rapid”
One instance is mapped to one or multiple VLANs
Needs additional configuration

## Slide 9: PVST+: Root switch per VLAN
Switch 2
Switch 3
Vlan 1
Vlan 2
Priority: 0
Priority: 4096
Priority: 32768
Priority: 32768
Priority: 0
Priority: 4096
R
R
Switch 1
Vlan 1
Vlan 2
Vlan 1
Vlan 2
port 1
port 2
port 1
port 2
port 1
port 2

## Slide 10: MSTP: Root switch per instance

## Slide 11: MSTP instances
By default all VLANs exist inside Instance 0 (a.k.a. IST)
The benefit of MSTP comes when:
    There are multiple VLANs
    Other (custom) instances are created
    VLANs are distributed across instances
    Different priorities are set for the different instances
    All switches are in the same region

## Slide 12: MSTP configuration
All switches in the MSTP domain must be in the same region
Three parameters should be configured equally on all switches:
    Configuration Name (region name)
    Revision number
    VLAN-to-instance mappings
    The priorities are configured on a per instance basis

## Slide 13: MSTP: All switches in the same region

## Slide 14: MSTP: Multiple regions

## Slide 15: MSTP defaults
On many switches, when spanning tree is enabled, they use MSTP by default …but there is no custom MSTP configuration
So each switch will be in its own region and CST (RSTP) will run between these switches

## Slide 16: MSTP defaults (2)

## Slide 17: MSTP vs PVST+
Two similar protocols, which one is better?
PVST+ advantages:
  triggers STP calculation only if there is a potential loop in a particular VLAN
  detailed “look” of the network – does not block ports when there is no loop on the trunks for a given VLAN
  PVST+ disadvantages
  generates a lot of overhead in the network
  proprietary protocol

## Slide 18: MSTP vs PVST+ (2)
MSTP advantages:
    uses less BPDUs and generates less overhead
    open standard
    MSTP disadvantages:
    not VLAN aware (does not look which VLANs are on the trunk ports)
    Harder to configure
    Recommendation: use MSTP if you have more than 100 VLANs

## Slide 19
Link aggregation

## Slide 20: What is link aggregation?
Combination of two or more physical interfaces to create one logical link or port
Other terms with the same meaning:
  Port trunking (HPE Provision)
  EtherChannel (Cisco)
  Link bundling
  NIC bonding/teaming
  etc.

## Slide 21: Why to use link aggregation?
To increase the bandwidth
To provide redundancy

## Slide 22: Link aggregation protocols
Static (no protocol) option for link aggregation
LACP - IEEE 802.1AX (formerly 802.3ad)
  Static
  Dynamic
  PAgP - Cisco Proprietary
  Each protocol has configuration options for different scenarios
  LACP configuration and naming can be interpret (slightly) different between the vendors

## Slide 23: Interface requirements
In general, the physical interfaces which participate in a link aggregation group, should have the same:
  Speed
  Duplex
  VLAN
  All other settings – recommended

## Slide 24: Load sharing modes
  Multiple physical links form one logical but at the end the traffic uses the physical links
  Which exact link to use - random decision based on “conversations”
Conversations depend on the load sharing mode

## Slide 25
Device stacking: IRF

## Slide 26: What is device stacking?
One logical device
Combination of two or more physical devices to form one logical

## Slide 27: Why device stacking?
More resilient
Does not block ports (like STP)
Simple management
Simple design

## Slide 28: What is IRF?
IRF – Intelligent Resilient Framework
HPE proprietary stacking technology
Uses HPE Comware switches (or routers) only
The devices need to be from the same type
One device is elected as a master
The stack takes the master’s configuration

## Slide 29: Master election
When creating the IRF stack:
  The member with highest priority wins
  If no member has a higher priority, the member with the longest system up-time wins (rounded to 10 minutes)
  If no member has a longer up-time, the member with the lowest bridge MAC address wins
When joining another device to the IRF stack:
  The current master wins

## Slide 30: IRF ports and connections
SW-1
SW-2
SW-3
1/1
2/2
2/1
3/2
3/1
1/2
x/y
  Single physical cable Must be at least 10Gbps
  IRF port – memberID/port
Possible connections | 1/1 -> 2/2 | 1/2 -> 2/1
Not possible connections | 1/1 -> 2/1 | 1/2 -> 2/2
  Only connect IRF port 1 to IRF port 2!

## Slide 31: IRF topologies
SW-1
SW-2
SW-3
Daisy chain:
Ring:

## Slide 32: IRF split stack
When there is a split stack situation, each of the two parts assumes “I am the new master”
This can create problems
Additional Multi Active Detection (MAD) algorithm needs to be configured:
  LACP MAD
  BFD MAD
  ARP MAD

## Slide 33: Detect IRF split stack with LACP MAD
Additional Comware switch is required
Extended LACPDU are exchanged
If split stack, MAD triggers election
Smaller member ID wins
The other device(s) put in recovery state (shuts down the ports)
I am the master!
I am the master!

## Slide 34
Demonstration

## Slide 35: Summary
…
…
…
Spanning tree protocol advanced: MSTP and PVST+
Link aggregation
Device stacking technologies - IRF

## Slide 37: SoftUni Diamond Partners

## Slide 38: Educational Partners

## Slide 39: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 39