## Slide 1: OSPF advanced
Lecture 2
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Basic concepts and single area OSPF
Multi area OSPF
Connecting OSPF to external networks
LSA and area types
Demonstration

## Slide 3
Basic concepts and single area OSPF

## Slide 4: OSPF advantages
Fast convergence with triggered updates
Hierarchical structure (areas)
VLSM support (classless protocol)
Efficient communication with neighbors
Uses intelligent metric (cost)
Open standard

## Slide 5: OSPF disadvantages
Requires more RAM and CPU on the devices – maintains different tables (neighbor, topology, routing)
Requires good and careful design when multiple areas are needed
More complex to configure and troubleshoot

## Slide 6: OSPF terms
LSA – Link state advertisement
LSDB – Link state database
Router ID
Area
ABR – Area border router
Autonomous system
ASBR – Autonomous system boundary router

## Slide 7: OSPF terms: router ID
I have many names (interfaces), but just call me 2.2.2.2
Hi, 2.2.2.2!
Hi, 2.2.2.2!

## Slide 8: OSPF terms (2)
Autonomous system
ASBR
ABR
ABR
Area 0 = the backbone area

## Slide 9: Neighbor relationships
If multiple routers are connected to a switch, we use designated router (DR) and backup designated router (BDR)
This minimizes LSA traffic
Other routers are referred to as DROTHER (DR other)
The DR and the BDR ensure that all routers receive all the required updates

## Slide 10: Neighbor relationships (2)
The DR, the BDR and the DROTHERs
DR
BDR
DROTHER
DROTHER
DROTHER

## Slide 11: DR/BDR Election Process
  The first router that is active on the link becomes the DR
  The second router that is active on the link becomes the BDR
  Link/interface priority is used for a re-election if the DR/BDR fails
  Default priority is 1
  Highest priority is elected; if a tie, the highest router ID (not IP address on the interface) is elected
  A priority of 0 prevents a router from becoming a DR or BDR

## Slide 12
Multi area OSPF

## Slide 13: Why multiple areas?
When the OSPF domain is segmented to areas:
  Inter-area routes can be summarized
  Router’s LSDBs are not too big
  The protocol is faster
  Stability and control is increased

## Slide 14: Multiple areas example
  All other areas connect to Area 0 (the backbone area)
  ABR routers in the example:
    Router1
    Router2
    Router3

## Slide 15: How to configure an ABR
There is no specific command to become an ABR
When you configure a router in more than one area, it becomes ABR
Router1:
router ospf 1
network 10.0.1.0 0.0.0.255 area 0
network 10.1.1.0 0.0.0.255 area 1

## Slide 16
Connecting OSPF to external networks

## Slide 17: OSPF autonomous system and external networks
  ASBR routers in the example:
  Router1
  Router6

## Slide 18: Redistribute between protocols
You need to import or redistribute routes to your AS
Some options for redistribution:
  redistribute RIP
  redistribute ospf [process_id]
  redistribute static
  redistribute connected

## Slide 19
LSA and area types

## Slide 20: OSPF LSA types
LSA type 1: Router
LSA type 2: Network
LSA type 3: Summary
LSA type 4: ASBR summary
LSA type 5: ASBR external
LSA type 6: Multicast OSPF
LSA type 7: Not-so-stubby area LSA

## Slide 21: OSPF area types
Standard area
Stub area
Totally stubby area
Not-so-stubby area (NSSA) 

## Slide 22: OSPF stub area
Uses LSA types 1, 2, 3 + default route (for external networks)
Blocks LSA types 4 and 5
  Area 1 is stub
  Router1 injects:
  Routes from area 0
  Default route to externals

## Slide 23: OSPF totally stubby area
Uses LSA types 1 and 2 + default route (for the other areas and external networks)
Blocks LSA types 3, 4 and 5
  Area 2 is totally stubby Router2 injects:
  Default route to externals
  (everything outside of Area 2)

## Slide 24: OSPF not-so-stubby area (NSSA)
Uses LSA types 1, 2, 3 and 7
Blocks LSA types 4 and 5
  Area 3 is NSSA Router6 injects:
  Routes in AS2
  Router3 injects:
  Routes from other areas
  (Route to 82.15.15.0/24 not advertised)

## Slide 25: Common area types and LSAs
Stub Area
No LSA type 4
No LSA type 5
Totally Stubby Area
No LSA type 3
No LSA type 4
No LSA type 5
NSSA Area
Uses LSA type 7
No LSA type 5

## Slide 26
Demonstration

## Slide 27: Summary
…
…
…
Basic concepts and single area OSPF
Multi area OSPF
Connecting OSPF to external networks
LSA and area types
Demonstration

## Slide 29: SoftUni Diamond Partners

## Slide 30: Educational Partners

## Slide 31: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 31